AIRWORTHINESS NOTICES - B029, EDITION 2, 23 NOVEMBER 1998

406-MHz EMERGENCY LOCATOR TRANSMITTER REGISTRY REQUIREMENTS

(This Airworthiness Notice supersedes AN No. B029, Edition 1 dated 17 October 1995)

Introduction

The purpose of this Airworthiness Notice is to advise aircraft owners/operators and maintainers of the encoding protocols which are to be adopted for emergency locator transmitters (ELTs) which transmit on 406 MHz.

Background

In 1988 an agreement was signed between Canada, France, the United States, and the former USSR to implement the COSPAS-SARSAT program.  The COSPAS-SARSAT program incorporates satellites in near-polar and geostationary orbits to relay transmissions from emergency beacons to ground terminals.  The system is designed to operate with the latest generation ELTs which transmit on 406 MHz.  This frequency makes the ELTs more readily detectable by satellites than the 121.5-MHz ELT now in widespread use.  Coding information such as location, identification of the beacon, vehicle and its country of registration, can be included in the 406-MHz distress signal.  The ICAO and CARAC organizations are currently discussing the implementation and mandating the future use of this type of ELT.  Canadian Aviation Regulation (CAR) 605.38 is in the process of being amended to require the registration of this type of ELT.

Required Protocols

In order to obtain consistency in the protocols used in Canada, the following User and Location protocols shall be adopted by the aviation community.

User Protocols

ELT (AF)(AP)(AD)

406-MHz ELTs which are fixed to the aircraft, shall be programmed using the Serialized Aircraft 24-bit address format.  The country code shall reflect the state in which the aircraft is registered.  All Canadian registered aircraft currently have a unique 24-bit address assigned to them.  The aircraft 24-bit address is currently being used in other airborne systems such as TCAS, and provides the advantage of uniquely identifying the airframe in addition to the ELT.

ELT (S)

406-MHz ELTs which are not fixed to the airframe, and are intended for use in appliances such as life rafts, shall be programmed using the ELT serial number protocol.  The country code shall reflect the state in which the ELT is registered.  For initial installations, it is preferred that the country code reflect the state in which the aircraft is registered.  This protocol allows the ELT manufacture to uniquely identify each ELT which is produced, and allows more than one ELT of this type to be carried on an aircraft.

Location Protocol

Currently, some avionics systems have the capability of continuously updating the Fixed type ELT with the aircraft’s current position (Latitude and Longitude).  For aircraft whose avionics and installation support this capability, it is recommended that the Standard Location protocol be used in conjunction with the Serial Aircraft 24-bit address User Protocol.

ELT Registration

Manufacturers of 406-MHz ELTs that are approved by Transport Canada Civil Aviation will be required to include COSPAS-SARSAT registration forms with all ELTs sold in Canada.

Importing Aircraft into Canada

Aircraft owners and operators who import an aircraft into Canada shall ensure that the 406-MHz ELT meets, and is encoded to, the required protocols, and that the ELT is registered with the appropriate registry.

Change of Aircraft Ownership and/or Registration

The onus shall be placed on the purchaser or lessee to ensure that any changes to the 406-MHz ELT coded information is completed, and that the revised information has been brought to the attention of the Canadian Beacon Registry.  In the case of aircraft which are already equipped with survival type ELTs (ELT(S)), it is preferred that the country code be changed to reflect the state in which the aircraft is registered, and that the appropriate beacon registry be notified.

Benefits

It is anticipated that by maintaining a consistent coding standard within the country, the potential for duplicate codes is greatly reduced.  Further, with the cooperation of the aviation community, a current ELT database with the Canadian Beacon Registry could aid in reducing the time spent in obtaining information on a suspected downed aircraft.  Failure to register the ELT could result in delayed SAR response.

Further Information

For further information on the encoding standards please contact:

Transport Canada, Civil Aviation

Airworthiness Engineering - AARDD

330 Sparks Street

Ottawa, Ontario

K1A 0N8

For additional information on the COSPAS-SARSAT program please contact:

Canadian Beacon Registry

National Search and Rescue Secretariat

275 Slater Street, 4th Floor.

Ottawa, Ontario

K1A 0N8

Phone:  1-800-727-9414 or (613) 996-1504

For the Minister of Transport

K.J. Mansfield

Director, Aircraft Certification